Construction Contractor Compliance Checklist   SUR-CP001-6

To be completed by Contractor and forwarded to the DPTI Contract Manager with each project

Contractor:  	 Job No:

Project Description (Road Name):

|  | Compliance Codes | C - Complies | N - Non Compliance |  |
| --- | --- | --- | --- | --- |

| Clause | Heading or Description of Clause | Compliance | Details of Non Compliance (Attach separate statement if insufficient space) | Auditor Only |
| --- | --- | --- | --- | --- |
| Tender Documents | Party Leader Qualifications |  |  |  |
|  | WHS and hazards addressed |  |  |  |
|  | Field Audits/Contract Manager Notified |  |  |  |
| SUR-CP001 | Survey duties completed as required |  |  |  |
| Survey Standard | Marks placed conform to Detail Design Development |  |  |  |
|  | Pegs with brads or similar mark better than 10mm accuracy |  |  |  |
|  | Other marks better than 10mm accuracy |  |  |  |
| Horizontal Control | Control based on existing survey stations |  |  |  |
|  | Additional survey stations placed |  |  |  |
|  | Survey stations verified and recorded in ‘As Set-out’ report |  |  |  |
| Vertical Control | Control based on Deep Bench Marks |  |  |  |
|  | Control based on existing survey stations |  |  |  |
| Temporary Benchmarks | Established not more than 100 metres apart |  |  |  |
|  | Temporary Benchmarks witnessed |  |  |  |
|  | Temporary Benchmarks levelled twice |  |  |  |
|  | Two reduced level runs within 5mm |  |  |  |
| Witnessing | Marks placed |  |  |  |
|  | Painted yellow |  |  |  |
|  | Marked with Pt No. or chainage and offset |  |  |  |
|  | Witnessed with pickets in non trafficked areas |  |  |  |
|  | Driven flush in shoulders, lawns, footpaths etc. |  |  |  |
|  | Other marks ringed, chainage and offset painted yellow |  |  |  |
|  | All painting not obtrusive |  |  |  |
| Contractor to supply Safety & Service Division | Project Report including new stations |  |  |  |
| Attachment 'A' | ‘As Set-out’ Pegging Report |  |  |  |
| Attachment 'B' | 'As Set-out' Street Lighting Report |  |  |  |
| Attachment 'C' | 'Layer Verification' Report |  |  |  |
| Attachment ‘D’ | ‘DTM Layer Verification’ Report |  |  |  |
| Attachment ‘E’ | ‘Bench Mark Report’ |  |  |  |