Construction Survey Standard Specification - SUR-CP001

1.	GENERAL

This Standard Specification sets out the requirements for Construction Surveys.

The Contractor shall comply with the requirements of the following documents which are located from Road Design and Survey sections at: http://www.dpti.sa.gov.au/standards

Detail Design Development

Design to Survey Compliance Checklist

Construction Survey Compliance Checklist

Contract Review Form

Engineering Survey Standard Specifications

and

DP001 Design Presentation – Appendix A - DPTI Layer Matrix (Construction Drawings)

access document at: ftp://ftp.transportsa.com.au/tsa_techdata/CAD%20Support%20Files/CAD MATRIX.xls

2.	Construction Survey

A Construction Survey shall require the set-out of all strings and points as detailed in the contract documentation provided by DPTI Transport Services Division.

3.	Survey Standard

Pegs placed shall conform to the Road Design Standards and Guidelines as described in Design Development, Detail Design Development Section 3.1 & 3.2.

Pegs shall be marked with a brad or similar and this mark shall be placed to an accuracy of better than 10 mm.

If other marks are used they shall be placed to an accuracy of better than 10 mm.

4.	Horizontal Control

The horizontal control for each project shall be based on the existing survey stations.  The Contractor shall place additional survey stations (if required) with a unique number, refer to Engineering Survey Standard Specifications, Section 2 for numbering convention. At job completion include these in Survey Control section of project report.

The Contractor shall verify in the field all marks used to control each project and record in "As Set-out" pegging report (see Attachment A).

5.	Vertical Control

Deep bench marks that have been placed on a project shall be used for vertical control.  The levels of these marks shall be considered absolute.  All levelling carried out shall be based on these deep bench marks.

On projects where no deep bench marks exist, the vertical control shall be based on the existing survey stations.  The levels shall be based on a mark nominated by the Principal.  If no mark is nominated, a line of best fit between levels shall be adopted as the new level datum.

6.	Temporary Bench Marks

Temporary bench marks shall be established not more than 100 m apart and shall be stable enough to ensure that no vertical displacement occurs during construction of the project.  The marks shall be witnessed.

Temporary bench marks shall be levelled twice using differential levelling techniques (i.e. automatic level and staff) and the two reduced levels shall not differ by more than 5 mm.

7.	Witnessing Stamping and Painting of Marks

All marks placed shall be:

- Wooden/plastic pegs, droppers, metal pins, galvanised iron nails, spikes or drill holes

- painted yellow

- annotated with point number or chainage and offset

- witnessed with pickets in non trafficked areas

- driven flush in shoulders, lawns, footpaths and all other areas where pegs may create a hazard to pedestrians, animals and machinery if left above the natural surface.

All painting must not be obtrusive, but blend with the surrounds.

8.	Data Supplied by DPTI Transport Services Division

DPTI Transport Services Division will provide the following for each project:

- construction plans

- genio file or 12da file of strings and survey stations

- report of horizontal alignment (G strings, if available) showing tangent point chainages and centre of curve coordinates

- geometric documents report

- cross section report (if available)

- survey stations report in csv format.

9.	NAMING OF DESIGN MODELS IN GENIO OR 12DA FILE

A complete list of design strings is documented in ‘Detail Design Development’ referred to above. A summary of commonly used strings appears below:

Design Final

Commonly requested design strings used to form the design pavement surface (CE - Gutter Lip, LC - Control line level, MT - Median edge, MR - Bitumen edge wing, CI - inside bitumen edge).

Design Control

Commonly requested design control strings (MC - Alignment control, GC - Alignment control geometry, MA - Carriageway control, GA - Carriageway control geometry, MU - Linemarking control, GU - Linemarking control geometry MK - Other control, GK - Other control geometry).

Design Setout

Commonly requested set out strings ( XC - Kerb line offset, XD - Drainage pit orientation, XO - Kerb base extent, XL - Light pole orientation, XT - Traffic signal pole orientation, PLIG - Lighting pole, PPIT - Drainage structures, PRAM - Ramp cut out centre, PTSP - Signal Pole, XS - Full Depth Pavement Extents, PSSA - Survey control stations).

Design Drain

Commonly requested set out drainage strings (DI - Pipe invert or DB - Box culvert invert).

10.	PHYTOPHTHORA HYGIENE

Where a site has been identified by the principal as a high risk Phytophthora zone, the Contractor shall work in accordance with Operating Instruction 21.3 Appendix 3: Phytophthora Hygiene Procedure for Minor Works and Site Inspections. This instruction shall be followed if soil is sticking to equipment, footwear or vehicle tyres.

11. 	ITEMS TO BE SUPPLIED BY THE Contractor

The Contractor shall supply the following items:

Digital data in the form of either:

- A genio file or 12da file of all points set out placed in a model called “As Set out Model YYYY_MM_DD”.

Points set out shall match the string label in the design eg MR01 in the “As Set out Model” shall carry the same string label as MR01 in the Design Model. For offset lines drop off the first letter of the string and prefix with O i.e. OR01

- A genio file or 12da file of all points staked out using point string PUPL in a model called Layer Verification 270 Model, where 270 is the depth of layer below design

Project Report (presented in the following order):

- Table of Contents

- Location of survey, type and job number

- Survey Party Leader names and equipment used

- a report detailing verification of horizontal control marks used on the project, including any new survey stations placed

- a report of the temporary bench marks detailing chainage, offset, type of mark used (see Attachment E) and also a summary of the two levelling runs and the values adopted

- a copy of the levelling data file or field sheets

- an "As Set-out" Pegging Report (see Attachment A)

- Construction Survey Compliance Checklist for each stage of set-out

- a report of the level differences for Street Lighting (see Attachment B)

- a layer verification report (see Attachment C)

- a DTM Layer Verification Report (see Attachment D)

- All reports to be submitted within 48 hours of each stage of set-out

- A copy of the Contractor’s Traffic Management Plan.

All documentation shall be supplied in Microsoft Excel format.

The Contractor shall retain evidence to satisfy the requirements herein.  The evidence is subject to a random audit at the Contractor's premises by DPTI Transport Services Division.

Attachment A

"As Set-out" Pegging Report

Job Number and Description: xxxxxxxx

Contractor's Reference: xxxxxxxx

Survey date: xx/xx/xx

| Pt No | Survey Station | String Label | Chainage | Offset | As Set-out East | As Set-out North | Design East | Design North | Diff East Design-East As Set-out | Diff North Design-North As Set-out | Diff Staked Elevation-Design Elevation | Mark Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | S300 |  |  |  |  |  |  |  |  |  |  | Dropper |
| 17 |  | S001 |  |  | 37861.381 | 61981.184 | 37861.383 | 61981.187 | 0.003 | 0.003 | 0.100 | Dropper |
| 23 |  | S002 |  |  | 37919.007 | 62001.441 | 37919.010 | 62001.431 | 0.003 | -0.010 | 0.065 | Picket |
| 18 |  | MR01 | CH 160 | -25 | 37870.906 | 61985.126 | 37870.906 | 61985.128 | 0.000 | 0.002 | 0.043 | Paint |
| 19 |  | MR01 | CH 170 | -23 | 37880.395 | 61989.084 | 37880.405 | 61989.104 | 0.010 | 0.020 | 0.021 | Paint |
| 20 |  | MR01 | CH 180 | -19 | 37889.476 | 61995.081 | 37889.468 | 61995.083 | -0.008 | 0.002 | 0.007 | Picket |
| 23 |  | S002 |  |  | 37919.007 | 62001.441 | 37919.010 | 62001.431 | 0.003 | -0.010 | 0.002 | Picket |
| 17 |  | S001 |  |  | 37861.381 | 61981.184 | 37861.383 | 61981.187 | 0.003 | 0.003 | 0.005 | Dropper |

Attachment B

"As Set-out" Street Lighting Report

Job Number and Description: xxxxxxxx

Contractor's Reference: xxxxxxxx

Survey date: xx/xx/xx

| Survey Station | Point Id | As Set-out East | As Set-out North | Design East | Design North | Design Elevation | Staked Elevation | Diff East Design-East As Set-out | Diff North Design-North As Set-out | dH | Mark Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| S317 |  |  |  |  |  |  |  |  |  |  | PSM |
|  | S118 | 70418.654 | 50187.871 | 70418.655 | 50187.868 |  |  | 0.001 | -0.003 |  | Dropper |
|  | S314 | 70383.009 | 50569.285 | 70383.017 | 50569.272 |  |  | 0.008 | -0.013 |  | PSM |
|  | PLIG13 | 70400.343 | 50399.889 | 70400.345 | 50399.895 | 29.327 | 28.972 | 0.002 | 0.006 | 0.355 | Peg |
|  | XL131 | 70400.217 | 50401.419 | 70400.217 | 50401.412 | 29.327 | 28.784 | 0.000 | -0.007 | 0.543 | Peg |
|  | XL132 | 70400.480 | 50398.405 | 70400.478 | 50398.411 | 29.327 | 29.142 | -0.002 | 0.006 | 0.185 | Peg |
|  | S118 | 70418.654 | 50187.871 | 70418.655 | 50187.868 |  |  | 0.001 | -0.003 |  | Dropper |
|  | S314 | 70383.009 | 50569.285 | 70383.017 | 50569.272 |  |  | 0.008 | -0.013 |  | PSM |

Note: dH= Design Elevation - Staked Elevation

Attachment C

"Layer Verification" Report

Job Number and Description: xxxxxxxx

Contractor's Reference: xxxxxxxx

Survey date: xx/xx/xx

| SUBBASE 1 |
| --- |
| Depth: 0.250 m; Tolerance: ± 0.020 m |
| Pt No. | Survey Station | String Label | Chainage | Offset | Design East | Design North | Design Elevation | Staked Elevation | Diff Staked Elevation-Design Elevation | Outside Tolerance |
| 1 | S300 |  |  |  | 4923.981 | 10435.226 | 100.158 | 100.158 | 0.000 |  |
| 2 |  | S001 |  |  | 4920.138 | 10436.975 | 100.276 | 100.279 | 0.003 |  |
| 3 |  | S002 |  |  | 4919.300 | 10425.962 | 100.170 | 100.174 | 0.004 |  |
| 4 |  | NJ01 | 260.7 | -7.7 | 4915.576 | 10427.571 | 100.514 | 100.273 | -0.241 |  |
| 5 |  | NJ01 | 269.7 | -7.8 | 4911.720 | 10419.383 | 100.496 | 100.248 | -0.248 |  |
| 6 |  | CE01 | 269.8 | -12.2 | 4915.563 | 10417.388 | 100.367 | 100.132 | -0.235 |  |
| 7 |  | NJ01 | 279.8 | -7.8 | 4907.314 | 10410.340 | 100.470 | 100.202 | -0.268 |  |
| 8 |  | CE01 | 279.8 | -12.0 | 4911.094 | 10408.494 | 100.345 | 100.095 | -0.250 |  |
| 9 |  | NJ01 | 290.0 | -7.7 | 4902.883 | 10401.154 | 100.435 | 100.163 | -0.272 | 0.002 below |
| 10 |  | CE01 | 290.2 | -11.9 | 4906.568 | 10399.114 | 100.308 | 100.041 | -0.267 |  |
| 11 |  | CE01 | 300.5 | -12.1 | 4902.207 | 10389.840 | 100.282 | 100.006 | -0.276 | 0.006 below |
| 12 |  | NJ01 | 300.6 | -7.8 | 4898.312 | 10391.525 | 100.408 | 100.127 | -0.281 | 0.011 below |
| 13 |  | NJ01 | 310.0 | -7.9 | 4894.290 | 10383.028 | 100.395 | 100.108 | -0.287 | 0.017 below |
| 14 |  | CE01 | 310.2 | -12.5 | 4898.440 | 10380.904 | 100.256 | 99.970 | -0.286 | 0.016 below |
| 15 |  | NJ01 | 320.3 | -8.0 | 4889.985 | 10373.764 | 100.363 | 100.078 | -0.285 | 0.015 below |
| 2 |  | S001 |  |  | 4920.138 | 10436.975 | 100.276 | 100.279 | 0.003 |  |
| 3 |  | S002 |  |  | 4919.300 | 10425.962 | 100.170 | 100.174 | 0.004 |  |

Attachment D

"DTM Layer Verification" Report

Job Number and Description: xxxxxxxx

Contractor's Reference: xxxxxxxx

Survey date: xx/xx/xx

| DTM Layer Verification Report1 |
| --- |
| Depth: 0.270 m; Tolerance: ± 0.005 m |
| Pt No. | Survey Station | Point | Chainage | Offset | Design East | Design North | Design Elevation | Staked Elevation | Diff Staked Elevation-Design Elevation | Difference at layer Elevation |
| 1 | S300 |  |  |  | 4923.981 | 10435.226 | 100.158 | 100.158 | +0.000 |  |
| 2 |  | S001 |  |  | 4920.138 | 10436.975 | 100.276 | 100.279 | +0.003 |  |
| 3 |  | S002 |  |  | 4919.300 | 10425.962 | 100.170 | 100.174 | +0.004 |  |
| 4 |  | NJ01 | 260.7 | -7.7 | 4915.576 | 10427.571 | 100.514 | 100.273 | -0.241 | 0.029 above |
| 5 |  | NJ01 | 269.7 | -7.8 | 4911.720 | 10419.383 | 100.496 | 100.248 | -0.248 | 0.022 above |
| 6 |  | CE01 | 269.8 | -12.2 | 4915.563 | 10417.388 | 100.367 | 100.132 | -0.235 | 0.035 above |
| 7 |  | NJ01 | 279.8 | -7.8 | 4907.314 | 10410.340 | 100.470 | 100.202 | -0.268 | 0.002 above |
| 8 |  | CE01 | 279.8 | -12.0 | 4911.094 | 10408.494 | 100.345 | 100.095 | -0.250 | 0.020 above |
| 9 |  | NJ01 | 290.0 | -7.7 | 4902.883 | 10401.154 | 100.435 | 100.163 | -0.272 | 0.002 below |
| 10 |  | CE01 | 290.2 | -11.9 | 4906.568 | 10399.114 | 100.308 | 100.041 | -0.267 | 0.003 above |
| 11 |  | CE01 | 300.5 | -12.1 | 4902.207 | 10389.840 | 100.282 | 100.006 | -0.276 | 0.006 below |
| 12 |  | NJ01 | 300.6 | -7.8 | 4898.312 | 10391.525 | 100.408 | 100.127 | -0.281 | 0.011 below |
| 13 |  | NJ01 | 310.0 | -7.9 | 4894.290 | 10383.028 | 100.395 | 100.108 | -0.287 | 0.017 below |
| 14 |  | CE01 | 310.2 | -12.5 | 4898.440 | 10380.904 | 100.256 | 99.970 | -0.286 | 0.016 below |
| 15 |  | NJ01 | 320.3 | -8.0 | 4889.985 | 10373.764 | 100.363 | 100.078 | -0.285 | 0.015 below |
| 2 |  | S001 |  |  | 4920.138 | 10436.975 | 100.276 | 100.279 | +0.003 |  |
| 3 |  | S002 |  |  | 4919.300 | 10425.962 | 100.170 | 100.174 | +0.004 |  |

Attachment E

SURVEY BENCH MARK REPORT

Description:		_______________________________________________________

_______________________________________________________________________

_______________________________________________________________________

Abn: 92 366 288 135

| Chainage | Offset | Description | Reduced Level |
| --- | --- | --- | --- |