|  | Transport Services Division ROAD DESIGN Operational Procedures & Forms |
| --- | --- |

ELECTRICAL SERVICES: Presentation & Technical Review Checklist

Project No:  _______________________________________Patches:___________________

Consultant (if applicable)_______________________________________________________

Description__________________________________________________________________

___________________________________________________________________________

TRAFFIC CONTROL

| Refer to Presentation Review Checklist |  |  |
| --- | --- | --- |
| TRAFFIC SIGNALS- DP011 |  |  |  |  |
| TS notes |  |  |  |  |
| Legend |  |  |  |  |
| Phase diagram |  |  |  |  |
| Sign schedule |  |  |  |  |
| Line marking |  |  |  |  |
| Traffic control signs and code |  |  |  |  |
| Critical dimensions |  |  |  |  |
| Design vehicle noted |  |  |  |  |
| Show ‘No Stopping Any Time’ zones |  |  |  |  |
| Trimmed survey |  |  |  |  |
| Pole numbers |  |  |  |  |
| Tactile not on TS drawing |  |  |  |  |
| TS/PC design uses Combo’s wherever possible |  |  |  |  |

| TRAFFIC SIGNAL CONDUIT- DP012 |  |  |  |  |
| --- | --- | --- | --- | --- |
| TS Ducting Notes |  |  |  |  |
| Legend |  |  |  |  |
| Line marking on |  |  |  |  |
| Circuit Details or referenced to Lighting/Supply Dwg Legend |  |  |  |  |
| TS Pole numbers on |  |  |  |  |
| Pole schedule added |  |  |  |  |
| Conduit size and type |  |  |  |  |
| TS pits S & D located correctly, no pits (apart from detector) in islands. |  |  |  |  |
| Detector pits located at back of loop locations wherever possible |  |  |  |  |
| Switchboard location & ID Numbers added OK |  |  |  |  |
| Supply points SA Power Networks, Stobie or U/G specified |  |  |  |  |
| Isolation Pits located >5m from TS Controller |  |  |  |  |
| TS/PC design uses Combo’s wherever possible |  |  |  |  |
| Telstra Connection or 3G |  |  |  |  |
| UPS Added (New Installs only or as specified) |  |  |  |  |
| SC orientated correctly |  |  |  |  |
| ITS-DP0 (tba) |  |  |  |  |
| Legend added as either sheet or individual sheet |  |  |  |  |
| Network Schematic added (where reqd) |  |  |  |  |
| Circuit Details or referenced to appropriate Dwg |  |  |  |  |
| Pole schedule added |  |  |  |  |
| Conduit size and type |  |  |  |  |
| Pits located & displayed correctly, e.g. size or secure or lockable |  |  |  |  |
| ITS Isolation Pits added adjacent equipment |  |  |  |  |
| Switchboard location & ID Numbers added Metered? e.g. PDB-M? |  |  |  |  |
| Supply points SA Power Networks, Stobie or U/G specified |  |  |  |  |
| Circuit Details or referenced to Lighting/Supply Dwg Legend |  |  |  |  |
| On drawings display Upstream Device-Downstream Device-Cable Type Comms Type e.g. fibre (No)/radio+ any Elect feed. |  |  |  |  |
| ID Asset codes added e.g. VMS?/CMS?/VSS?/AWS? |  |  |  |  |
| Outstations displayed correctly (inc orientation and connections) |  |  |  |  |

| LIGHTING- DP013 & LD 001 |  |  |  |  |
| --- | --- | --- | --- | --- |
| Electrical Notes legend |  |  |  |  |
| Legends |  |  |  |  |
| Luminaire Nos added |  |  |  |  |
| Cable sizing OK |  |  |  |  |
| 1phase/3phase appropriate |  |  |  |  |
| Light pole structure numbers & cct designators |  |  |  |  |
| Cct loading OK |  |  |  |  |
| Cct details OK |  |  |  |  |
| Poles |  |  |  |  |
| TS/PC design uses Combo’s |  |  |  |  |
| SB/IA pole used at the correct location |  |  |  |  |
| Clearances to HV OK or OTR response |  |  |  |  |
| Poles not in conflict zones |  |  |  |  |
| Pole setback OK for road speed |  |  |  |  |
| Cables Conduit U/G |  |  |  |  |
| Pits OK & Lockable where CM used |  |  |  |  |
| 1x50, 1x80 used OK + spares |  |  |  |  |
| Sw/Bd in good location- for TS/PC use common Distribution |  |  |  |  |
| 50m spacing’s between poles or pits max |  |  |  |  |
| Cable sizing OK e.g. 6,10 or 16mm |  |  |  |  |
| Light schedules & Luminaire & pole type table |  |  |  |  |
| Light Luminaires correctly labelled & referenced to correct sheet |  |  |  |  |
| Line marking on |  |  |  |  |
| Symbols showing new lighting & upgrades |  |  |  |  |
| Symbols showing existing lighting to remain |  |  |  |  |
| Symbols showing conduit (including size) |  |  |  |  |
| Switchboard location & ID Number OK |  |  |  |  |
| Supply points SA Power Networks, Stobie or U/G specified |  |  |  |  |
| Luminaire sizing & pole ‘H’ appears to be OK for the application |  |  |  |  |
| Bracket Check feedback required |  |  |  |  |
| Asset numbers added. |  |  |  |  |

| Checked …………………...... Designer …………………...... |  |  |  |  |
| --- | --- | --- | --- | --- |
| Signed.................................... Technical Reviewer............................... |  |  |  |  |
| Designer................................. Issues Addressed............................... |  |  |  |  |